Part II: Calorimeter Technologies
Homogeneous calorimeters
  1. Scintillating crystals
  1. Lead glass (Čerenkov light)
Sampling calorimeters
  1. Active media
    1. Plastic scintillator
    1. Ionization chambers
        1. Noble gases
        1. Noble liquids
    1. Semiconductors
  1. Passive media
    1. Choice of density
    1. Choice of Z, A

---
Homogeneous Calorimeters
Scintillation Light
All shower particles
lose energy only via
interactions with the
absorber, which is
also the active material,
so
e / mip = 1
Čerenkov Light
LR(cm)
LR(cm)

---
CLEO CsI Crystal Calorimeter
7800 thallium-doped CsI Crystals

---
CLEO CsI Crystals
 Each crystal 5 cm square by 30 cm (16 LR) long
Silicon photodiode readout

---
CLEO CsI Energy Resolution
CsI: QWG3 Topical School.
B Heltsley, LEPP.
Beijing, Oct 2004
Energy resolution

---
Crystal Calorimeter Spectroscopy
(2S) Inclusive  Spectrum
CsI: QWG3 Topical School.
B Heltsley, LEPP. Beijing, Oct 2004

---
CMS PbW04 EM Calorimeter
76000
 Lead tungstate crystals

---
CMS Crystal Production
Automated quality control
Light yield
Light transmission
Radiation hardness
12th International Conference on Calorimetry in High-Energy Physics
Chicago, Illinois, 6-9 June 2006

---
CMS PbW04 Test Beam Performance
Alexandre Zabi
12th International Conference on Calorimetry in High-Energy Physics
Chicago, Illinois, 6-9 June 2006

---
Sampling Calorimeters

---
Electromagnetic Sampling Fraction
Energy resolution scales with the inverse
square root of the sampling fraction.
ZEUS (U): fem= 4%
Compensation can be achieved in lead,
but since it produces fewer neutrons
than uranium, fem must be reduced
and so the resolution suffers.
In this case, the thickness of the absorber
was doubled and the thickness of the
scintillator halved.

---
e/h Ratio and Compensation
Rel: Ionization signal from relativistic charged pions
P: Ionization signal from spallation protons
n: Signal from evaporation neutrons
inv: energy deposited with no signal, e.g. nuclear recoil
So e/h can be determined if the sampling fractions of these components
relative to the MIP sampling fraction are known.
(ref:Wigmans)

---
Consequences of Differing
Sampling Fractions fEM and fH
Signal fluctuations are not gaussian
Fluctuations in EM part affect overall resolution
Signal is not proportional to E
Ratio of signal for electrons and hadrons depends on energy
Relative resolution does not scale with E-1/2
Purely hadronic component
 component
 Calorimeter response relative to MIPs

---
Response Nonlinearity from Noncompensation
Intrinsic e/h
The signal from pions
approaches that for
electrons as the em fraction
of the shower increases
with energy.
Sπ / Se
Intrinsic e/h
The linearity of the signal
from pions is poor for the
same reason.
Sπ

---
Energy Resolution for Noncompensation
Statistical term
Scale with √E
10%
Energy-
independent
term
0%

---
Low-energy hadrons and MIP's
At low energy (E<5 GeV), hadrons lose more of their energy via ionization than via shower formation and nuclear interactions. As a result, even compensating calorimeters exhibit nonlinearity at low energy. Since an essential characteristic of a compensating calorimeter is a lower sampling fraction for e and h than for mips, the sampling fraction decreases with hadron energy.
ZEUS, 1990

---
Ways to reduce fem
Absorb the e+e- pairs from low energy photons in the passive material. If one uses a high-Z material, not only are more low-energy photons produced, they are also preferentially absorbed in the high-Z material (photo-effect), AND the e+e- they produce can't get out of it. For example, for 511 keV photons, f/fmip=0.27 in uranium and 0.83 in steel. In this manner, the overall fecan be reduce 30-40%.
Wrap the passive material in a material of lower Z. The thickness can be tuned to absorb photoelectrons and reduce their contribution. ZEUS used 0.3 mm stainless steel cladding to reduce fe by 10%.
(ref:Wigmans)

---
Ways to increase fh
Add hydrogenous materials to increase sensitivity to neutrons via elastic neutron-proton collisions. Note that this method is more effective for lower sampling fractions.
  1. Use scintillator (ZEUS, H1 spaghetti calorimeter)
  1. Add hydrogen rich gas admixture for wire chambers (L3, e.g. C4H10)
Increase integration time to be sensitive to slow nuclear processes (D0, ≈ 1 μs)
(ref: Wigmans)

---
The ZEUS Detector

---
ZEUS Uranium/Scintillator Calorimeter
3.2 mm U + 2.6 mm Sci
fe = fh = 4%
fmip = 7%
MIP sampling fraction
U: 1.09 MeV/(g/cm2) x 18.65 g/cm3 = 20.3 MeV/cm
Sci: 1.95 MeV/(g/cm2) x 1.0 g/cm3 = 1.95 MeV/cm

---
ZEUS Calorimeter Sampled Signal
JAC, International Workshop on Calorimetry in High-Energy Physics, Brookhaven (1994)

---
Calibration Techniques
Test Beams
Cosmic muons
Laser/LED Monitoring
Guided 60Co sources
Low-level, stable radioactive background
In situ physics (0, , Ze+e-, -symmetry, ...)
Cell-weighting to optimize resolution, uniformity
(ref: Wigmans)

---
ZEUS: Muons wrt Uranium Noise

---
ZEUS EM Cell Test Beam Calibration Uniformity
Contribution to the
energy-independent
term in the resolution

---
ZEUS e/h and Energy Resolution

---
CMS Laser Monitoring of PbW04 Crystal
Light Transmission
Recall goal of 0.5% systematic contribution to energy resolution, which limits dynamic range of precise measurement
Short-term radiation damage affects light transmission at a greater level than this, and varies from crystal to crystal
Laser-based monitoring system has been developed which will monitor the transmission properties of each crystal at the 0.1% level over ten years
Adi Bornheim
12th International Conference on Calorimetry in High-Energy Physics
Chicago, Illinois, 6-9 June 2006

---
Concluding Remarks
Since the 1980's, calorimetric measurements have grown in importance with the expanding energy frontier in elementary-particle physics, becoming the precision instrument of choice due to their exploitation of high-statistics counting methods
Intense R&D programs have improved quantitative understanding of the physics behind their operation (e.g. measurements of hadronic showers in the mid 1980's) and resulted in a huge variety of available calorimeter technologies
Today's applications of calorimeters extend from medical diagnostics to neutrino astrophysics, from satellites to deep-sea arrays, from mountaintops to Antarctic ice.
The experimental particle physics community has reached a consensus to expand the energy frontier as necessary to understand electro-weak symmetry breaking, entailing an enormous global effort to build a linear electron-positron collider. Present estimates of the necessary energy measurement precision exceed the capabilities of existing calorimeters by substantial factors. Extensive detector-development programs are in preparation around the world, inspiring confidence in a bright future for progress in calorimetry and further expansion of its range of applications.

---
End of Section
on
Calorimeter Types
and
Calibration Methods

---
Sampling Calorimeters

---
Hadronic Showers