## Slide 1
Ring Commissioning

## Slide 2: Outline
Diagnostics
  Injection Beam Monitor System (injection line)
  Fiber harps (storage ring)
Variables
  M5 line final focus quadrupoles
  M5 line horizontal and vertical dipole correctors
  Inflector B-field
  Kicker timing and amplitude (X3)
  Quad voltage (X4)
Strategy
  Transmission through injection line
  Optimizing capture and storage in ring

## Slide 5: Commissioning
1X1mm2 clad square scintillating fibers
Entrance to iron
Entrance to inflector
Inflector exit
Scinitillating fiber detectors
=> Centroid and size

## Slide 6: Commissioning
Entrance to iron
Entrance to inflector
Inflector exit
Procedure for tuning injection line trajectory
Center beam on D1 by tuning vertical and horizontal offset with upstream steerings
Center on D2 by tuning vertical and horizontal angle with steerings
Adjust inflector field to center on D3

## Slide 7: Commissioning
Entrance to iron
Entrance to inflector
Inflector exit
Procedure for tuning final focus
Measure vertical and horizontal beam size on each detector
Adjust upstream quads as required

## Slide 8: Commissioning
4 - Fiber harps are flipped into the ring for injection tuning.
2 vertical horizontal pairs at
180 deg and 270 deg

## Slide 9: Commissioning
Tuning ring kickers
Adjust 3-independent kickers to minimize injection oscillations
Fiber harps give turn by turn position of beam centroid
  Measure dependence of turn by turn horizontal position on each of 3 kickers by varying kicker fields
  Dependence of position on kick is inverted to give kicks that center the beam
  M5 beam line steering can be used to center beam vertically
FFT of position of centroid on fiber harps => betatron tune
  Adjust electrostatic quadrupoles to set tune
FFT of beam width => beta mismatch and energy spread

## Slide 10: Commissioning
Tune
Initial angle offset (upstream steerings)
Inflector field
Kicker fields
To maximize capture and minimize CBO

## Slide 11: Commissioning

## Slide 12: Storage ring optics
Weak focusing
Uniform vertical magnetic field
4 – electrostatic quadrupoles – each with arc length of 39 deg, equally spaced around the ring
Qh=0.904, Qv = 0.433

## Slide 13: Injection aperture
Apertures
Inflector half-width = 9mm
Inflector half-height = 28mm
Storage volume radius = 45mm

## Slide 14: Mismatch
Disparate apertures suggest varying b-functions
With mismatch of twiss parameters at inflector-ring interface, peak b & h in the ring are always greater than closed ring values
=>
Mismatch example
Inflector exit

## Slide 15: Acceptance
We maximize transmission and capture by focusing the beam so that inflector and ring have equivalent acceptance
The maximum in the ring depends on the matching according to
Then
We find that inflector and ring have equivalent acceptance if

## Slide 16: Dispersion
=>
Energy acceptance of inflector and ring are equivalent if
and since
=>
Tracking simulations indicate optimal capture for
The energy acceptance follows from

## Slide 17: Injection Channel
We need to understand how to propagate distribution through injection channel so that at the inflector exit

## Slide 18: Injection Channel
Muons come to the end of the M5 line and then propagate through:
Hole in magnet yoke
Dipole fringe field
Inflector
And exit the inflector 77 mm from the center of the dipole aperture
The magnetic field is near zero at the inner surface of the yoke, and rises to 1.45T between the magnet poles, over a distance of ~39cm
39cm

## Slide 19: Magnetic field through Injection Channel
The vertical magnetic field of the dipole and the inflector along the axis of the injection channel separately(left) and summed(right). The horizontal component is zero due to midplane symmetry. There is net steering and significant focusing
- Horizontally defocusing, vertically focusing
De-focusing in dipole fringe field

## Slide 20: Inflector field gradient
Inflector field map
There is some uncertainty regarding magnitude of the gradient in the inflector.

## Slide 21: Injection channel defocusing
The 4.3m injection channel can be modeled as follows
drift
quad
Qfringe(k=-0.36)
1.6m
1.3m
1.7m
quad
Qinf(k=-0.16)
Dipole fringe and inflector overlap
Or we can compute the transfer maps numerically by tracking

## Slide 22
18mm inflector
inflector | bx (inc) | ax (inc) | by (inc) | ay (inc) | hx (inc) | h'x (inc) | bx (exit) | by (exit) | hx (exit)
E821(WG inf) | 53.1 m | 15.9 | 3.96 m | 3.53 | 0 | 0 | 1.5m | 10m | 0
E821(unif-inf) | 37.72 | 10.82 | 0.958 | 1.15 | 0 | 0 | 1.5m | 10m | 0
Propagating b through injection channel
Match at entrance to magnet iron, depends on inflector gradient
Extremes are indicated
2% gradient
0 gradient
Hole through iron
fringe

## Slide 23
Larger aperture inflector requires
adjustment of
incident offset and angle (to center beam in aperture)
b,h functions at inflector exit
kicker field
Larger aperture inflector

## Slide 24
36mm inflector
inflector | bx (inc) | ax (inc) | by (inc) | ay (inc) | hx (inc) | h'x (inc) | bx (exit) | by (exit) | hx (exit)
36mm | 41.8 m | 11.2 | 1.2 m | 2.0 | 5.2m | -1.34 | 5m | 16m | 2m
Propagating b through injection channel
With a larger aperture inflector,
bx increases to 5m
h Increases to 2m
(assume zero gradient in inflector)

## Slide 25
In view of various tradeoffs, identification of optimum focusing, angle and offset at entrance to injection channel, kicker field and timing, quad voltage, etc. are best determined by simulation.
The simulation requires a model
We have developed both a GEANT based model and a BMAD model
Model:
Injection channel (yoke, fringe, inflector) characterized in terms of field maps
Multiple scattering in the coils overlapping the entrance and exit of the inflector (effectively increasing emittance)
Kicker field map based on real plate geometry
Quadrupole fields represented by multipole expansion
Multiple scattering of muons that enter storage region through quad plates
Collimators define storage region aperture
Muons that hit the inner walls of the inflector or the storage ring collimators are assumed lost
Muons that survive 20 turns are captured
Injection Simulation

## Slide 26: Muon distribution
MARS and G4beamline used to simulate pion production, focusing by Lithium lens, collection of muons from pion decay and transport to ring
dE/E < 2%
e0 ~ 50 mm-mrad
This raw distribution is the starting point for simulation of injection into ring

## Slide 27: Initialization of Injection Simulation
Compute s-matrix of the raw distribution. Extract e, bx,by,ax,ay h,d
Create matrix R(braw > binf)
Compute matrix R(bM5 > binf) for propagation from end of M5 line through injection channel to the inflector exit
Transform raw distribution as follows:
  Xstart = R(braw > binf) R-1(bM5 > binf) Xraw
  The distribution Xstart tracked to the inflector exit will have the desired binf,ainf,hinf
Set initial offset and angle with respect to reference trajectory
Set inflector field, kicker field, pulse width, quad voltage etc.
Track muons through injection channel into and around the ring
Muons that survive 20 turns are stored

## Slide 28: Initialization of Muon Distribution
Raw distribution projected to match point just upstream of entrance to ring magnet iron
inflector | bx (inc) | ax (inc) | by (inc) | ay (inc) | bx (exit) | by (exit)
E821(WG inf) | 53.1 m | 15.9 | 3.96 m | 3.53 | 1.5m | 10m
bx =1.5m, by =10m at inflector exit
Propagation through injection channel
18mm inflector
Hole through iron
fringe

## Slide 29
Evolution over first 20 turns

## Slide 30
Tuning: kick, bx, by, and h

## Slide 31: Distributions before and after
Initial distribution projected to inflector exit
Distribution of muons that survive tracking through injection channel
Distribution of muons that survive 20 turns
h=0
±0.5%

## Slide 32
Lost muons
E821 inflector
36mm inflector
3.92% stored
7.31% stored

## Slide 33: Initial angle and offset
“tune” steering magnets in the M5 line to determine optimum offset and angle of incoming muons (muons surviving 20 turns are “captured”)
Dx’ ~ 0.5 mrad
Dx ~ 3mm
Vary Dx and Dx’ with respect to reference trajectory

## Slide 34: Tune b and h at inflector
Muons are either
Lost in the injection channel
Lost in the ring
Or captured
By increasing h and b in the inflector (“tuning” M5 quads), particles that otherwise would be lost in the ring (and into the calorimeters) are scraped away upstream
Maximum capture
b=1.5m
h < 2 m
Minimum lost in ring
h = 2 m

## Slide 35
Summary
Inflector and ring apertures are very different
Twiss parameters in the inflector are chosen to maximize transmission and capture
Propagation of twiss parameters backwards to entrance into backleg iron defines matching requirements
The range of matching conditions is specified to include flexibility to accommodate 18mm inflector with or without gradient, as well as a 36mm inflector
Simulations based on detailed models of injection channel and storage ring are used to guide the optimization of parameters (tuning)
  Steering and Focusing at end of M5 line
    Dx and Dx’ at entrance to backleg iron
    b and h at inflector
  Inflector field
  Kicker parameters
    Field and timing for each of the 3 kicker pulsers
  Quadrupole voltage
Providing dependencies of
Capture efficiency
CBO amplitude and modulation of beam width and height
Characteristics of stored beam and lost particles
Two distinct models have been developed, based on BMAD and GEANT respectively, are in reasonable good agreement

## Slide 36: END

## Slide 37
30 cm upstream of yoke
inflector | Offset[cm] | Angle[mrad]
e821 | -4.77 | 22.4
36mm | -2.90 | 17.9
Trajectory

## Slide 38
E821 inflector
36mm inflector
inflector | bx (inc) | ax (inc) | by (inc) | ay (inc) | bx (exit) | by (exit)
e821 | 53.1 m | 15.9 | 3.96 m | 3.53 | 1.5m | 10m
36mm | 41.8 m | 11.2 | 1.2 m | 2.0 | 5m | 16m

## Slide 39
30 cm upstream of yoke
Entrance to iron
Entrance to inflector
Inflector exit
Silicon detectors ?
=> Centroid and size

## Slide 41
Entrance to iron
Inflector upstream
Inflector downstream
End 200 turns
Evolution of distribution through injection channel and around ring

## Slide 42: Trajectory through injection channel
There is a unique combination of initial offset Dx and angle Dx’for the injected beam that exits along the axis of the inflector.
(Steering magnets near the end of the M5 line provide the flexibility to maximize transmission by tuning Dx and Dx’)

## Slide 43
Includes scattering & 989 kicker field
No scattering & 989 kicker field
No scattering & uniform kicker field
Dependence of optimum by at the inflector on scattering and kicker field profile
Conclusion: Soft dependence on by . Peak is near 10m.
Note that ring by = 15.5m. Larger by increases losses in inflector

## Slide 44: Radial beam motion
Beam exits yoke
Beam through outer coil
Beam through Inflector
Beam kicked onto orbit

## Slide 45: Propagating twiss parameters
To propagate twiss parameters through the injection channel it is convenient to construct a transfer matrix.
The transport is roughly equivalent to
Drift – Quad – Drift
where the quad G ~ 3.7T/m
In practice we determine the transfer matrix (M) by numerically computing the phase space mapping in the neighborhood of the reference trajectory.

## Slide 46
Inflector Aperture
Aperture
Inflector ax= ±9mm,ay= ±28mm
storage ring ±45mm
To clear the inflector aperture
bx ≤ 2m, (by = 17m)
h ≤ 1.8m

## Slide 48: Storage Ring Kicker Requirements
Kickers steer injected muons onto the closed orbit of the storage ring
Requirements:
Kick angle ~ 10.8 to 12.1 mrad
Kicker B-field ~ 218 to 245 Gauss
Integrated B-field ~ 1.11 to 1.25 kG-m
Pulse width(τwid)
120ns < τwid < 149ns
Repetition rate
~100Hz peak, 12Hz average
3 – 1.7m kickers
d = 77 mm, R=7112 mm
kick angle q = d/R = 10.8 mrad
trev = 149 ns

## Slide 49
Larger aperture inflector
Existing inflector
Larger aperture inflector requires
Adjustment of incident offset and angle (to center beam in aperture)
Increased kicker field
Phase Space Matching