## Slide 1: Decoherence of CBO
D. Rubin
March 24, 2015

## Slide 2: Decoherence
Betatron tune (number of wavelengths/turn) is determined by quadrupole voltage
  V=± 31kV => Qx = 0.90386 Qy = 0.43271
  frev = 6.71 MHz
  fh = Qx frev , fy = Qy frev
An amplitude dependence results from quad nonlinearity
Energy dependence due to chromaticity
  Qx’ = -0.14 Qy’ = 0.31

## Slide 3: Damping
No real damping.
  Amplitude of oscillation of each muon is COM
Muons with different amplitude and energy decohere
Decoherence time [turns] ~ 1/DQ

## Slide 4: Amplitude dependent tune

## Slide 5: Amplitude dependent tune
Oscillation of single muon with and without quad 10 pole term
4mm peak-to-peak

## Slide 6: Envelope of difference => DQ
Difference with and without quad 10 pole term
(4mm peak-to-peak)
180 deg out of phase after 420 turns

## Slide 8
No quad multipoles and no energy spread
Time dependence of centroid and width

## Slide 9
Time dependence of centroid and width
All quad multipoles included. Zero energy spread
10mm peak-to-peak
20mm peak-to-peak

## Slide 10
  Qx’ = -0.14 Qy’ = 0.31
Energy dependent tune
DE/E = ± 0.002 => DQ ≈ (DE/E) Qx’ ≈ (2)2.8 E-4 = 1/1785
=> Decoherence time due to energy spread ~ 1785 turns

## Slide 11
Single muon energy ±0.002

## Slide 12
Difference of DE/E = ± 0.002

## Slide 13
Decoherence due to energy dependent tune
se/E = 0.00112
No quad multipoles

## Slide 14: Energy and amplitude dependence
se/E = 0.00112
All quad multipoles

## Slide 15: Conclusion
Amplitude dependence
(No energy spread)
Energy dependence
(No multipoles)
Chromatic decoherence time ≈ 1000 turns
Amplitude dependent decoherence time (due to quad nonlinearity) ≈ 2000 turns
(Betatron modulation more effectively damped by amplitude dependence)