## Slide 1
Muons into inflector – 10000
40 mm-mrad emittance
0.15% energy spread
= 2m at inflector
at inflector is optimized
Kick is optimized
821 inflector horizontal aperture =18mm
989 inflector horizontal aperture = 36mm
Kicker fields are fitted analytic expansion to map computed with femme
No scatter in quad or kicker plates is included
Muons surviving 20 turns are defined as “captured” (vast majority of muons lost are lost in the first few turns)

## Slide 2
Sub_dir | inflector | End scatter | Kicker field | Muons captured | Betax for max capture (M_cap) | Betax for Max M_cap/CBO_Amp
20140211 | 821 | Yes | E989 | 1165 | 2.825 | 2.825
20140211-1 | 821 | No | E989 | 1637 | 2.225 | 5.225
20140211-2 | 989 | Yes | E989 | 1816 | 2.825 | 3.425
20140211-3 | 989 | No | E989 | 2586 | 4.025 | 6.5
20140211-4 | 989 | No | E821 | 2975 | 3.625 | 8.
20140212-1 | 989 | Yes | e821 | 2192 | 2.425 | 4.425
20140211-6 | 821 | Yes | 821 | 1403 | 2.225 | 2.425
20140211-7 | 821 | No | 821 | 1891 | 2.025 | 6.425
20140211-5 | 989 | No | Uniform | 3002 | 3.625 | 8.
20140211-8 | 821 | Yes | Uniform | 1447 | 2.025 | 4.825
20140211-9 | 821 | No | Uniform | 1912 | 2.025 | 7.625
20140212 | 989 | Yes | Uniform | 2255 | 3.225 | 7.025
10000 particles
20 turns
eta=2.0 at inflector exit.
Gaussian phase space with 40 mm –mrad emit, 0.0015 energy spread
Scan 2. < betax < 8
Optimize kick

## Slide 3
20140211-5

## Slide 4
Dependence of number of muons captured and CBO amplitude on e821 kicker field
With 10000 muons incident at inflector
Minimum CBO amplitude/max capture at 215 gauss
Assumes e821 inflector and includes scattering in inflector end coils

## Slide 5
20140211