## Slide 1
Injection Study Plan
D. Rubin and N. Froemming
October 9, 2013

## Slide 2
Goal:
Determine optimal injection efficiency with CD1 equipment
Develop machinery for evaluating impact of variations in beam parameters or hardware like
  Scattering in inflector end coil
  Bigger inflector aperture
  Kicker field profile and time dependence
  Kicker location
  Beam parameters at entrance to ring
  etc.

## Slide 3
Emittance, energy spread, and length and longitudinal distribution of the bunch at the upstream end of the inflector
Twiss parameters at the inflector exit including α,β,η,η’, both horizontal and vertical
Kicker amplitude, field uniformity and temporal dependence. Also the longitudinal location (along the central orbit) of the midpoint of the kick
Quadrupole voltage and field uniformity
Inflector aperture and end coil that overlaps aperture, inflector swing angle and tilt
etc.
Dependencies

## Slide 4
Each set of parameters can be characterized in terms of
Fraction of muons that are transmitted through the inflector
Fraction of muons that are stored - (those that survive ~100 turns)
Energy spread of stored muons
Fraction of muons that clear inflector aperture that are ultimately lost in the ring. (Small is presumably better)
Amplitude of coherent betatron oscillation of the centroid of the bunch
Depth of modulation of the bunch height and width, and frequency of the modulation
Characterization

## Slide 5
Model
Model (based on Cornell BMAD accelerator library routines) ring includes:
Uniform dipole field
ES quadrupoles (field represented as power series expansion based on plate voltage)
  Plan to use a map for quad number 1 with plate at larger offset
Kicker (uniform with time dependence as E821 RLC type or rectangular)
  Coding more realistic spatial and temporal dependence
Runge-Kutta tracking through E&M fields

## Slide 6
Initial beam distribution
Suppose particles are all produced when a beam of protons strikes a circular disk
1 mm radius target
Assume emittances εx εy will be transported to the ring
Gaussian in x and y with σx and σy = 1 mm => βx βy
Gaussian energy spread and that there is no correlation of energy with position (η=0)
Bunch length is likewise uncorrelated with energy
Construct the transfer matrix from the production target to the inflector in terms of α,β, and η at the inflector exit.
The result is a ~ realistic distribution at the inflector

## Slide 7
Input Parameters
Twiss parameters at inflector exit
{

## Slide 8
Distribution of particles at the inflector exit
(before eliminating those outside inflector aperture)
10,000 particles

## Slide 9
1559 particles
Distribution of particles after 100 turns

## Slide 10
Turn by turn average x,y,l,dp/p
Turn by turn σ x,y,l,dp/p

## Slide 11
Number of particles remaining after each turn
After inflector

## Slide 12
Plan
Explore dependencies on all input parameters – beginning with perfect kicker
  (10,000 particles and 100 turns takes a few seconds)
Identify (by some optimization algorithm) the “best” configuration
  highest capture efficiency with
  Minimum betatron oscillation and modulation and
  Minimum number of lost muons in the ring
Re-optimize with more realistic kicker (and es quads)
Find optimum with larger aperture inflector
Meanwhile
Incorporate realistic kicker and quad fields in gm2_ring_sim
Add turn by turn evaluation of beam centroid and “size” to gm2_ring_sim

## Slide 13
eta = 0, dp/p=0.5%
eta = 8m, dp/p=0.5%
Dependence on dispersion at inflector