## Slide 1: Scraping and lost muons
D. Rubin
October 6, 2016

## Slide 2
E821 quad scraping strategy:
At injection, inner and outer and top and bottom quad plates are powered asymmetrically
The closed orbit is displaced from the center of the storage volume by about 2.5mm.
The effective aperture is reduced by the offset of the closed orbit – so that muons outside the reduced aperture are scraped off and removed from the distribution
Quad symmetry is restored after 30 ms (200 turns).
Closed orbit is restored to the midplane and magic radius.
Leaving 1.25 mm clearance between the extreme of the distribution and the aperture as defined by the collimators

## Slide 4
Modeling quadrupoles with independently powered plates
Solve Laplace eqn for quad with a single plate at voltage and the remaining 3 at ground – for each of the four plates in turn
=> 4 maps
Linear combination of the 4 maps scaled by relative voltage yields effective dipole kick and quadrupole focusing

## Slide 5
Tunes at Injection Tunes after ramp
Qx 0.9137 0.9039
Qy 0.4090 0.4403
Closed orbit, tunes, and b at injection and after ramp
Closed orbit after ramp at 0
 | Top | Bottom | Inner | Outer
Q1 | 32 | 22.7 | -32 | -32
Q2 | 32 | 22.7 | -22.7 | -32
Q3 | 32 | 22.7 | -32 | -32
Q4 | 32 | 22.7 | -32 | -22.7
Quad voltage at injection

## Slide 6
injection
E821 Quad voltage ramp
store

## Slide 7
At t=0, inject muons on displaced closed orbit.
Track 1000 turns
Quad plate voltage ramps as in E821
(Plot shows orbit at exit of Q4 on each turn)
Orbit shifted to center of aperture as quads ramp to nominal (symmetric voltage)
A small horizontal betatron oscillation is introduced by the ramp

## Slide 8
Simulation of injection, scraping and capture
Distribution at end of M5 line is generated with
95% emittance ~ 40 mm-mrad
1.1 % energy width
3% energy cutoff
120ns pulse length with ‘W’ distribution
Distribution is tracked through backleg, fringe, inflector, with scattering in end coils
Kicker
field profile as computed
Temporal profile as measured
Quads
2 D field maps of each plate at V with others at 0 superposed for scraping
Initial Scraping voltages 71% of full voltage
Full voltage corresponds ~ to field index 0.185

## Slide 9
Distribution at end of M5 line
100,000 muons

## Slide 10
Phase space at inflector exit
67522 muons

## Slide 11
Phase space after one turn in ring
6345 muons

## Slide 12
Phase space after 100 ms
5003 muons

## Slide 13
Sum of 10 runs, 1 E6 muons total at end of M5 line
Of the 50k stored, 2 muons are lost in the interval between the end of scraping at 30ms
and end of tracking at 104 ms (700 turns)
Approximately 100 muons
are lost in the interval 10 – 100 ms as shown at right
n=0.185, V=32 kV

## Slide 15
No scraping
n= 0.175, 30.3 kV
Muons remaining -> 100 ms
Collimator misalignment
scraping

## Slide 16
n=0.185, 32 kV
No scraping
Apply scraping voltage anti-symmetrically -> steering but no tune shift
Vin -> Vin + DV, Vout-> Vout - DV
Vbot-> Vbot + DV, Vtop-> Vtop - DV
Standard asymmetric scraping

## Slide 17
Quad misalignment?
Quad offsets | X[mm] | Y[mm]
Q1 short | 1 | 0
Q1 long | -1 | 0
Q2 short | 0 | 1
Q2 long | 0 | -1
Q3 short | 0 | 1
Q3 long | 0 | -1
Q4 short | 1 | 0
Q4 long | -1 | 0

## Slide 18
Summary