## Slide 1: Kicker Status
A. Mikhailichenko, D. Rubin
Cornell
March 26, 2015

## Slide 3: Kicker Magnet
10.8 mrad kick corresponds to 1114 kg-m
  292 G for each of 3 - 1.27m long kicker magnets
  0.4 mm thick plates
  Magnet geometry => 65G/kA
  => 4.5 kA/kicker magnet
  => 56 kV on each Blumlein
“New” larger aperture inflector” requires 12mrad kick
  => 62 kV / Blumlein

## Slide 4: Current Generator
12.5 Ω Blumlein triaxial transmission line
Assembled from 6 – 60 inch sections (20 ns/section) (30 ft long)
Filled with Castor oil, ε=4.7, (pulse length τ α √ε) (as compared to Corning 561 silicon oil, ε=2.7)
Concentric tubes are separated with teflon standoffs (we plan to replace with macor)
Two grid(fast) thyratron – rated for up 70kV – 15kA (7.5 kA in load)
Coupled via 4 parallel 50Ω coaxial cables and resistors (12.5 Ω equivalent) to the kicker magnet

## Slide 5
12.5 Ω Blumlein triaxial transmission line

## Slide 6: Thyratron switch

## Slide 8: Thyratron and charging input

## Slide 9: Blumlein schematic
12.5 Ohm Blumlein
3500A X 12.5W = 43.75kV
Four parallel 50 W coaxial cables couple 12.5W
Blumlein to load

## Slide 11
Kicker chamber
Magnetometer laser
Vacuum pump
Load resistors in flourinert
4 parallel 50Ω cables

## Slide 12
Blumlein business end

## Slide 14: 4 –parallel coax to load

## Slide 15
Resistors are cooled in flourinert
Vacuum chamber

## Slide 16: Coupling to magnet
4 load resistors
4 50Ω coaxial cables
Vacuum chamber
flourinert

## Slide 17
Load resistors cooled in flourinert

## Slide 19: Coupling from Blumlein to Load

## Slide 24
Pearson 3212 current monitor;
Current in a 40 –cm long kicker;
Current value ≈ 2.4 kA;
Charging Voltage≈30 kV;
40ns/div
Pearson 3212 current monitor;
Current in a 40 –cm long kicker;
Current value ≈ 2.4 kA;
Charging Voltage≈30 kV;
100 ns/div
Same pulse
different time scale

## Slide 25
Pearson 6600 current monitor;
Current ≈2 kA; V ≈25 kV
Kicker length ≈ 60 cm;
40 ns/div, 12 Hz
Max current allowed by Pearson 6600
is 2 kA
Pearson 3212 current monitor;
Current ≈2 kA; V ≈25 kV
Kicker length ≈ 60 cm;
40 ns/div; 12 Hz
Max current allowed by Pearson 3212 is 7.5 kA
The same charging voltage, but different current monitors

## Slide 26
Pearson 3212; 50 kV; 4kA; 12 Hz, Kicker length ≈127 cm (50”)
The tail generated by slight mismatch of impedances.

## Slide 27: Kicker pulse
Mismatch (Blumlein to coax)
  Impedance matching chamber
  Alternative high voltage coax
Tail
  Charging circuit
Rise and fall time
  Kicker length
Width
  Blumlein length

## Slide 28
Proposed Impedance matching tuner
Includes resistor ( ~ 500 Ω) and capacitance or diode
Impedance Match

## Slide 29
Proposed Impedance matching tuner
Includes resistor ( ~ 500 Ω) and capacitance or diode
Match Blumlein impedance to cables
Impedance Match

## Slide 30
Alternative coax ?
Fermilab cable
Cornell cable
Impedance Match

## Slide 31: Charging circuit
HV transformer in oil
To Blumlein

## Slide 32
Moment of thyratron triggering
Current in primary windings
(Power Designs CVT-1A)
Voltage applied to Blumlein
(Voltage at secondary windings)
Current in secondary windings
Charging transformer characteristics contributing to signal after main pulse?
Charging circuit

## Slide 33: Rise/fall and width
Kicker inductance limits rise and fall
  Inductance proportional to length
  E821 - 3 X 1.7m long magnets
  Requisite 1114 kG-m is realized with
  3 X 1.27 m kickers at 4.5 kA (56kV)
  (leaving 1.2 m of the kicker chambers is unoccupied)
  Faster rise and fall can be achieved by further reducing kicker length and adding additional units to maintain integrated field (access into vacuum chamber?)
Width can be increased by adding sections to Blumlein
(space ?)

## Slide 34
Design for mounting kickers in cages

## Slide 35: Summary
30 ft 12.5 Ω Blumlein tested
  To 4kA (50kV) into 1.27m long kicker (briefly at 12 Hz)
  To 70kV with shorter kicker
Impedance transformer to improve match designed
Charging circuit contribution to tail under investigation
Kicker pulse
  Sufficient amplitude with 1.27m kicker but slow rise and fall limit width at full field
  Solution: Longer Blumlein and/or additional shorter kickers

## Slide 36
Current in primary windings
(Power Designs CVT-1A)
Current in secondary windings
(Pearson 410)
Moment of thyratron triggering

## Slide 42: Storage Ring Kicker Requirements
Kickers steer injected muons onto the closed orbit of the storage ring
Requirements:
Kick angle ~ 10.8 to 12.1 mrad
Kicker B-field ~ 218 to 245 Gauss
Integrated B-field ~ 1.11 to 1.25 kG-m
Pulse width(τwid)
120ns < τwid < 149ns
Repetition rate
~100Hz peak, 12Hz average
3 – 1.7m kickers
d = 77 mm, R=7112 mm
kick angle q = d/R = 10.8 mrad
trev = 149 ns

## Slide 43: 476.3.5.3 – Kicker Plate Design
Current feed from PFN
Crossover at end of strip line
Trolley rail
Kicker plates mounted in ring vacuum chamber
3 sets of strip line kickers
Length = 1.7m each
E 821 plates
E 989 plates
E989 plates and trolley rails

## Slide 44: 476.3.5.4 – Pulse Forming Network
Thyratron switch shorts middle conductor of triaxial line to outer conductor
Charging voltage
Blumlein pulse forming network
Coax cable couples blumlein center conductor to load
Load resistor matches impedance of Blumlein
Current pulse into a matched load computed with equivalent discrete circuit model
Width of pulse is proportional to length of Blumlein
40ns
Requirements:
3.5 kA
120ns width

## Slide 45: 476.3.5.4 – Pulse Forming Network
Kicker plates
Load resistor
thyratron
Blumlein
Load resistance matched to impedance of Blumlein
Pulse width
L = 9m
= 4.7 (Castor oil)
=> t = 120ns
Blumleins in storage ring hall

## Slide 46: Modeling of Kicker-pulser
B field current ratio => 1kA = 65G
CST Microwave Studio