## Slide 1
A. Mikhailichenko, D. Rubin
VACUUM CHAMBER IN A KICKER Telephone meeting September 16 2014

## Slide 2
Vac chamber wall
E-821 rail in a ring (except the kicker region)
New rail
Aluminum part made with longitudinal interruptions
Macor
Al
Al
In a Vacuum Chamber meeting on August 19 2014 we introduced the concept of rail design in a kicker region

## Slide 3
Procedure:
1) Drill holes through
2) Make threads
3) Close with short threaded cork
4) Weld cork outside
5) Shave outer surface

## Slide 4
Critical dimensions are the radiuses of rails
As the rails have a curvature with definite radius, the chamber itself should be aligned properly

## Slide 5
Isometric view of rails and HV plates in a chamber

## Slide 6
Just rails…
Macor posts
Macor wheels over posts

## Slide 7
The concept was tested at kicker model
Macor posts screwed into the wall

## Slide 8
E-821 rails in a region of the kicker plates
Cage attached to the chamber by screws
Vertical
fixators

## Slide 9
Principle of operation of vertical fixators is very simple:
Important to have an access from one side

## Slide 10
Thin wall cylindrical posts
Radial fixators
Vertical fixators
We considered a cage concept of installation of rails and HV plates also

## Slide 11
Two concepts in comparison
Semi-transparent vacuum chamber is shifted down for better visibility
Pretty flexible base

## Slide 12
Original shape (flat)
Shape after temperature changed (cooled)
For Al α=22e-6oC, L=200mm, ΔT=10o h≈2mm
For a 1oC the change is h≈0.6 mm
Sagitta appearance as a result of chamber shrinkage
Base plate of cage
ΔL= L-L'
One comment…

## Slide 13
CONCLUSIONS
Two concepts considered.
• Cage system demonstrates difficulties in keeping vertical positioning at
all length of the rails, as it fixes the cage position in few points only
• No direct connection of inner rails location and outer surfaces of the
chamber in a cage attachment
• Temperature dependence is more pronounced for the cage system
• More details required for the cage system
• Time consuming procedure of cage alignment
In some sense the chamber itself serves as a cage in our concept.
Further remarks are welcomed…

## Slide 14
Backup slides